## Slide 1
Impacts of SWCPs on sediment trapping, landscape disconnectivity & sustainable reservoir use, NW Ethiopia
Mulatie Mekonnen

## Slide 2
Introduction
The northwest highlands of Ethiopia are the major water sources of Abay River/GERD
More than 80% of the water is from these highlands

## Slide 4
Besides the highlands are
Suitable for human settlement (>60% popn)
Origins of many crop & tree species
Most suitable for agriculture, agriculture
widely practiced, etc.

## Slide 5
However;
Land degradation in the form of soil erosion, soil fertility depletion, water resources reduction, forest deterioration, etc.
is a prime problem in the highlands

## Slide 6
Consequently:
Reservoirs/lakes sedimentation
Reduced agricultural productivity
Infrastructures damage, etc.
are common problems

## Slide 7
To halt such nature devastating problems:
SWCPs both physical, biological & bio-physical have been practiced for half of a generation age
4 - 5 decades

## Slide 8
However,
The natural resource conservation & management works aren’t sustainable,
Farmers’ are destructing the constructed SWCPs claiming lack of benefits,
Like:

## Slide 9
Landscape dis-connectivity/
Slope gradient reduction,
Soil loss reduction
Soil fertility improvements
Crop productivity increment, etc.

## Slide 10
Hence,
The objectives of this investigation in the
Koga catchment representing the northwest highlands of Ethiopia is,

## Slide 11
To investigate the impact of SWCPs on sediment trapping, slope gradient reduction & Maize grain yield improvement

## Slide 12
Methodology
Field experiment
Field measurement
Field observation
Statistical analysis
GIS software
SPSS

## Slide 13
Results
SWCPs are trapping a dry sediment of:
26 - 44 kg m-1 yr-1
~55 kg m-1 yr-1 ( Mekonnen et al. 2016)
~ 25 kg m-1 yr-1 (Mekonnen & Getahun, 2020)
STE ~54%

## Slide 14
< 5 yrs old SWCPs
SB with retention basin trapped more sediment than FJ ridge
Reason, availability of the retention basin with enough space to trap sediment,

## Slide 15
> 10 yrs old SWCPs
FJ ridges trapped more sediment than SB
Reason, retention basin was filled by sediment & STE of SB reduced
No maintenance
But STE of FJ increased

## Slide 16
SWCPs are reduced slope gradient by:
1.2 % (below 5 yrs)
2.2% (5 - 10 yrs)
3.2% (10 - 20 yrs)
2-3 % in 20 yrs (Mekonnen et al. 2016)

## Slide 17
SWCPs are improving crop yield by:
~ 920 kg ha-1 yr-1 Maize
~700 kg ha-1 Barley (Mulat et al. 2020)
10 -15% (Teshome et al. 2013)
ETC.

## Slide 18
On the contrary,
No significant soil loss reduction
Water reservoirs sedimentation is high
Farmers are using the same rate of fertilizer as before

## Slide 19
Nutrient load to water reservoirs is high & causing weed emergency
like water hyacinth
In general land degradation is still a prime problem

## Slide 20
Highlands degradation

## Slide 21
Rivers carrying sediment to water reservoirs NW highlands of Ethiopia

## Slide 22
Rivers carrying sediment to water reservoirs NW highlands of Ethiopia

## Slide 23
Impact of sedimentation on water reservoirs
Koga man-made reservoir

## Slide 24
Conclusion
Although the existing SWCPs are
Trapping large amount of sediment,
Reducing slope gradient/landscape
connectivity,
Increasing crop yield,
etc.

## Slide 25
Soil erosion not significantly reduced
Sedimentation is critical,
Slope gradient is not minimized,
Land degradation is the main problem
After half of a generation age

## Slide 26
So What ???

## Slide 27
Therefore,
Researchers & experts, are expected to develop alternative approaches or modify the existing practices, after half of a generation age experience.

## Slide 28
Thank you