## Slide 1: Analaysis of the impact of Land use change and climate change on the Blue Nile River using SWAT
Sead Ahmed Swalih
Istanbul Technical University
August 2020

## Slide 2
Introduction
Problem statement and objectives
Materials and methods
Results and discussion
Conclusion and recommendations
1
2
3
4
5

## Slide 3: Introduction
Analysis of the impact of land use change and climate change on Blue Nile river using SWAT
NILE
WHITE NILE
BLUE NILE
World’s climate - changing & expected to continue in the coming century
Africa - most vulnerable to climate change and variability
The Nile basin, the largest basin in Africa – high topographic and climatic variability
  Increase vulnerability

## Slide 4
Introduction
Problem statement and objectives
Materials and methods
Results and discussion
Conclusion and recommendations
1
2
3
4
5

## Slide 5: Problem statement
high development on the Nile, i.e. construction of the Aswan Dam, Sennar, and Rosieres reservoirs for irrigation and hydropower generation
increased demand for irrigation and hydropower Ethiopia - GERD
high vegetation degradation in Ethiopia, i.e. deforestation, results in land use change
  ecosystem degradation due to massive utilization of river waters in Sudan and Egypt, eg. loss of biodiversity
increasing water demand upstream + climate change and land use change
Notes: Health issues are also important
  their impact on water resource sustanabily downstream need to be assessed

## Slide 6: Objectives
Assessing the dynamics of climate in the Basin
Projecting basin hydrology using climate change and land use change scenarios to assess their impacts

## Slide 7
Introduction
Problem statement and objectives
Materials and methods
Results and discussion
Conclusion and recommendations
1
2
3
4
5

## Slide 8: Study area
The Blue Nile River
  Blue Nile (in Amharic Abbay/in Arabic the Al Bahr al-Azraq)
    1529 km long (longest in the world)
    elevation of the basin varies from 4000m (little Abbay) to 700m at foot of the plateau
    contribute for 60 % flow of Nile
    crucial for thesurvival of downstream countries

## Slide 9: Study area cont’d
Chart: Land use/cover
| SAVA | CRDY | WATB | CRWO | GRASS | BSVG
Land use | 65 | 21 | 7 | 4 | 1 | 1
SAVA – Savanah forest
CRDY – Crop land/Dry land
WATB – Water body
CRWO – Crop land/Wood land
GRASS – Grassland
BSVG – Bush land vegetation

## Slide 10: Study area cont’d
Climate varies from humid to semiarid
  Kiremt …(Jun-Sept)
  Bega ……(Oct-Jan)
  Belg …….(Feb-May)
For the year 1961-1990,
  Annual preciptation was 1200mm to1600mm
  Annual temprature-was 18.3°C (2°C seasonal variation)
Chart: Preciptation %
| Belg | Kiremt | Bega
 | 16.9014 | 69.7183 | 13.3803

## Slide 11: Materials
Climate change scenario data
  Source: IPCC data distribution centre
  SRES-AR4 scenario runs of six AOGCMs were chosen
    BCM2_BCCR … abbreviated as BCM2 (Norway)
    CSIRO_MK3 ……. “ “ CSMK3 (Australia)
    INMCM3 ………… “ “ INCM3 (Russia)
    GISAOM …………. “ “ GIAOM (USA)
    MIROC3_2HI ….. “ “ MIHR (Japan)
    MIROC3_2MED.. “ “ MIMR (Japan)
    Preciptation and Temprature projections for 2020, 2055 and 2090 were analysed for storylines A1B and B1
Notes: A1- A future world of very rapid economic growth, low population growth, rapid introduction of technologies with convergence among regions and increased cultural interactions.
A1B- A future world of very rapid economic growth, low population growth and rapid introduction of new and more efficient technology.

## Slide 12: Materials cont’d
Preciptation change
Temprature change
Chart: MIMR



2020 | -23.9583 | 73.4211 | -2.271 | -6.0626 | -19.9801 | -7.7424 | 4.9181 | 14.4527 | 27.6936 | 25.9812 | -14.612 | -19.3819
2055 | 46.8333 | 3.3041 | 27.6986 | -10.3248 | -15.1743 | -11.3927 | 22.3787 | 15.3431 | 34.6362 | 25.5767 | -0.56005 | -18.9167
2090 | 2.7917 | -10.5556 | -7.3288 | -27.6496 | -24.9886 | -16.2397 | 9.0734 | 18.781 | 54.8278 | 47.0011 | -16.3959 | 25.125
Chart: MIMR
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2020 | 0.49668 | 0.34401 | 0.29786 | 0.63539 | 0.87501 | 0.59659 | 0.50519 | 0.24955 | 0.09914 | 0.34585 | 0.58097 | 0.56075
2055 | 1.492 | 1.4436 | 1.039 | 1.4705 | 1.7331 | 1.3309 | 1.0993 | 0.75871 | 0.77131 | 1.1478 | 1.3786 | 1.5256
2090 | 2.2696 | 2.2644 | 2.1124 | 2.644 | 2.7983 | 2.5118 | 2.3467 | 1.8548 | 1.632 | 2.2503 | 2.5354 | 2.6954

## Slide 13: Materials cont’d
Preciptation change
Temprature change
Chart: MIHR
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2020 | 36.2346 | 6.9209 | 9.5262 | 53.4004 | 2.3483 | -2.6954 | -9.5562 | 2.1314 | -6.2071 | 23.6216 | 7.5188 | 42.5941
2055 | 45.0926 | 0.63559 | -4.8199 | 11.3262 | 7.1786 | -8.3742 | -4.5129 | 8.081 | 25.9893 | 55.7103 | -9.1922 | 68.3495
2090 | 30.3704 | -38.5146 | -31.6304 | 0.2138 | -0.66937 | -13.3839 | -0.010808 | 14.0027 | 24.7992 | 50.9936 | 0.11228 | 66.9086
Chart: MIHR
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2020 | 1.4851 | 1.1156 | 1.5819 | 1.1191 | 1.2154 | 1.5497 | 1.4747 | 1.2079 | 1.3322 | 1.4946 | 1.5931 | 1.6934
2055 | 2.9716 | 2.1816 | 2.8159 | 2.8904 | 2.6178 | 2.991 | 2.7044 | 2.3522 | 2.1647 | 2.6004 | 2.8452 | 3.0896
2090 | 4.1226 | 3.7026 | 4.2957 | 4.2215 | 4.1228 | 4.3265 | 4.0006 | 3.3572 | 3.3904 | 3.7741 | 4.3211 | 4.4188

## Slide 14: Materials cont’d
Preciptation change
Temprature change
Chart: BCM2
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2020 | 2.483 | 12.6068 | 25.1382 | 0.96495 | -4.6087 | -8.3382 | -3.4517 | -8.7535 | 2.3036 | -21.0605 | 2.2069 | -6.7407
2055 | -12.1088 | -4.8504 | -7.7493 | 12.6469 | -14.0896 | -19.7838 | -12.3165 | -8.9236 | -1.1445 | 10.9731 | 11.0318 | 8.2963
2090 | -12.9592 | 47.6923 | -1.1738 | -47.1325 | -10.9593 | 3.7252 | -14.9437 | -11.0734 | -13.8323 | -15.3408 | 22.3743 | 13.963
Chart: BCM2
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2020 | 1.0717 | 0.90219 | 0.85882 | 1.2086 | 0.97932 | 0.83276 | 1.3212 | 0.70428 | 0.92136 | 1.1449 | 0.88302 | 0.96257
2055 | 1.6431 | 2.0043 | 1.4274 | 2.3816 | 2.134 | 2.0295 | 2.2088 | 1.7772 | 1.8472 | 1.8385 | 1.7869 | 1.9042
2090 | 2.69 | 3.0232 | 2.5695 | 3.6792 | 3.2389 | 2.8394 | 3.2738 | 2.7333 | 3.2198 | 3.0726 | 2.7315 | 2.7599

## Slide 15: Materials cont’d
Land use and cover (LUC) change scenario data
  Two hypothetical LUC scenarios for 2080 assuming + 10% change on savana forest
  It has also been assumed that change in SAVA (savana) cover will be compensated by CRDY (crop land/ dry land)
    LUS-1……. Land use scenario 1 - 10% increase in SAVA
    LUS-2 …… « « « 2 - 10% decrease «

## Slide 16: Materials cont’d
Chart: Land use
| SAVA | CRDY | WATB | CRWO | GRASS | BSVG
Land use | 65 | 21 | 7 | 4 | 1 | 1
LUC-1 | 75 | 12 | 6 | 4 | 1 | 1
LUS-2 | 57 | 31 | 6 | 3 | 1 | 1
Change in land use percentage

## Slide 17: Methods
Observed Flow
SWAT Model
Observed Baseline Precip.
IPCC AR4 Baseline Precip.
Observed Baseline Temp.
IPCC AR4 Scenario Temp.
IPCC AR4 Scenario Precip.
IPCC AR4 Baseline Temp
)
Bias Assessment for GCM uncertainty
Bias Assessment for GCM uncertainty
SWAT Model
Baseline Flow
Analysis & comparison
Scenario Flow
Input Data
Output Data
Processes
Model bias Correction
Model bias Correction
Corrected flow (1961-90)
Corrected flow (2011-99)

## Slide 18: Approaches
Model evaluation
Climate change anaysis
Land use and cover (LUC) change analysis
Land use change analysis coupled with climate change

## Slide 19
Introduction
Problem statement and objectives
Materials and methods
Results and discussion
Conclusion and recommendations
1
2
3
4
5

## Slide 20: Results
Model evaluation
Climate change anaysis
Land use and cover (LUC) change analysis
Land use change analysis coupled with climate change

## Slide 21: Results cont’d
Global water balance
  Preciptation……………………1026.1mm
    Surface runoff……………………208.6mm
    Lateral discharge……………….7.6mm
    Shallow aquifer recharge….120.1mm
    Deep « « ……………46.0mm (5%)
    Total aquifer recharge……….300.3mm
    Totla water yield……………….273.4mm
    ET……………………………………..509.3mm
    PET……………………………………2185.4mm
    Transmission loss………………7.0mm
The water balance closes with about 7% error

## Slide 22: Results cont’d
Annual yield

## Slide 23: Results cont’d
Annual yield

## Slide 24: Results cont’d
Annual yield

## Slide 25: Results cont’d
Annual yield

## Slide 26: Results cont’d
Seasonal flow
Chart: ROSSEIR
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Observed | 353.1 | 360 | 292.3 | 234.9 | 308.5 | 630.1 | 2458.9 | 5204.2 | 3713.5 | 1758.1 | 832.6 | 464.3
SWAT | 597.4 | 312.66 | 146.05 | 133.63 | 380.4 | 545.4 | 2810.9 | 4269 | 3656 | 1806 | 851.1 | 607.8
Notes: Peak flows have been underestimated

## Slide 27: Results cont’d
Seasonal flow
Chart: Khartoum
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Observed | 137.7 | 110.9 | 113.3 | 168 | 195.8 | 294.4 | 1588.2 | 5229.2 | 3927.1 | 1803.4 | 571 | 231.9
SWAT | 585.7 | 427.3 | 255.7 | 115.59 | 116.6 | 338.7 | 1457.7 | 4028 | 4118 | 2705 | 1811 | 1051.6

## Slide 28: Results cont’d
Statisticla indices

## Slide 29: Results cont’d
Statistical indices

## Slide 30: Results cont’d
Statistical indices

## Slide 31: Results cont’d
Statistical indices

## Slide 32: Results cont’d
Model predictive range
Chart: ROSSIER
Max | 600 | 600 | 330 | 289 | 534 | 703 | 4530 | 7910 | 5740 | 2900 | 1300 | 639
Min | 574 | 52.6 | 37.2 | 35.4 | 222 | 255 | 619 | 2270 | 1860 | 1280 | 647 | 0.3264
Observed | 353.1 | 360 | 292.3 | 234.9 | 308.5 | 630.1 | 2458.9 | 5204.2 | 3713.5 | 1758.1 | 832.6 | 464.3
Baseline Average | 597.4 | 312.66 | 146.05 | 133.63 | 380.4 | 545.4 | 2810.9 | 4269 | 3656 | 1806 | 851.1 | 547.8326

## Slide 33: Results cont’d
Residual analysis
Chart: ROSSEIR
Chart: ROSSIER

## Slide 34: Results cont’d
Residual analysis
Chart: KHARTOUM
Chart: Months

## Slide 35: Results cont’d
Residual analysis
Chart: SENNAR
Chart: Month

## Slide 36: Results cont’d
Model evaluation
Climate change anaysis
Land use and cover (LUC) change analysis
Land use change analysis coupled with climate change

## Slide 37: Results cont’d
Chart: BCM2
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
A1B | -8.2086 | 26.8946 | -27.1681 | -15.3602 | -5.8001 | -10.2487 | -14.7444 | -9.663 | -5.7604 | -18.7806 | 17.4524 | 13.6296
B1 | -6.8481 | 10.0712 | 37.9782 | -6.9868 | -13.9717 | -6.0159 | -5.7302 | -9.504 | -2.6884 | 1.8285 | 6.2895 | -3.284
Preciptation

## Slide 38: Results cont’d
Chart: BCM2
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
A1B | 2.1143 | 2.2651 | 1.9117 | 2.642 | 2.4698 | 2.0756 | 2.6097 | 2.0494 | 2.2494 | 2.3105 | 2.1681 | 2.2533
B1 | 1.4888 | 1.688 | 1.3255 | 2.2043 | 1.765 | 1.7255 | 1.9262 | 1.4271 | 1.7429 | 1.7269 | 1.4329 | 1.4978
Temprature

## Slide 39: Results cont’d
GCM uncertainty
Bias
Water yield

## Slide 40: Results cont’d
Base period
Chart: Discharge (m³/s)
max | 600 | 600 | 443 | 354 | 916 | 2730 | 7330 | 8330 | 8120 | 4320 | 2140 | 1110
min | 600 | 126 | 39.4 | 104 | 293 | 600 | 3150 | 4290 | 4140 | 1570 | 694 | 600
Observed | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333
BCM2 average | 600 | 448 | 298.5667 | 255.5 | 593.5 | 1490.3333 | 4821.6667 | 6635 | 6631.6667 | 2986.6667 | 1437.6667 | 760

## Slide 41: Results cont’d
Base period
Chart: Discharge (m³/s)
max | 600 | 600 | 248 | 402 | 815 | 991 | 4080 | 8160 | 8100 | 4490 | 1790 | 822
min | 600 | 94.3 | 39.3 | 130 | 319 | 561 | 1350 | 4600 | 4450 | 1940 | 785 | 600
Observed | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333
MIMR average | 600 | 340.8833 | 118.6833 | 259.8333 | 526.6667 | 701.1667 | 2656.6667 | 5676.6667 | 5845 | 2966.6667 | 1143.8333 | 658.6667

## Slide 42: Results cont’d
Base period
Chart: Discharge (m³/s)
max | 835 | 1320 | 2300 | 2810 | 2280 | 2280 | 7250 | 9840 | 9200 | 7670 | 3810 | 2180
min | 600 | 255 | 56.5 | 317 | 265 | 600 | 2140 | 4470 | 3770 | 2310 | 797 | 600
Observed | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333
MIHR average | 676.1667 | 650 | 1484.5833 | 1401.8333 | 1199.5 | 1381 | 4698.3333 | 7376.6667 | 7023.3333 | 4555 | 2180.1667 | 1242.8333

## Slide 43: Results cont’d
Average flow change
Chart: 2020
| BCM2 | CSMK3 | INCM3 | GIAOM | MIMR | MIHR
Average | 1450.7597 | 1504.6215 | 1789.3563 | 1842.2702 | 1994.8403 | 1571.7215
Minimum | 1091.771 | 1062.5909 | 1255.9203 | 1363.9071 | 1373.8329 | 1166.9399
Maximum | 1898.1696 | 1900.4338 | 2105.6854 | 2196.4193 | 2341.7578 | 1939.5842
Base | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375

## Slide 44: Results cont’d
Average flow change
Chart: 2055
| BCM2 | CSMK3 | INCM3 | GIAOM | MIMR | MIHR
Average | 1305.5136 | 1530.5933 | 1766.8548 | 1230.5784 | 1947.1422 | 1850.7491
Minimum | 1028.0623 | 1106.5766 | 1271.3948 | 931.1871 | 1418.8773 | 1323.148
Maximum | 1728.8796 | 1938.4758 | 2097.2424 | 1643.1079 | 2310.7794 | 2189.9374
Base | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375

## Slide 45: Results cont’d
Average flow change
Chart: 2090
| BCM2 | CSMK3 | INCM3 | GIAOM | MIMR | MIHR
Average | 1178.1648 | 1321.688 | 2071.7367 | 1584.8568 | 2321.601 | 1706.1554
Minimum | 905.1224 | 1021.574 | 1419.2625 | 1210.1557 | 1673.2648 | 1344.4503
Maximum | 1644.0973 | 1769.0118 | 2395.4846 | 1953.1794 | 2755.5876 | 2144.8436
Base | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375 | 1509.375

## Slide 46: Results cont’d
Seasonal flow change
Chart: 2020
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
BCM2 | 597.1667 | 281.5 | 70.05 | 52.6667 | 388.3333 | 593.1667 | 2398.3333 | 4623.3333 | 4063.3333 | 1626.6667 | 809.8333 | 609.6667
CSMK3 | 590.75 | 259 | 66.25 | 53.0167 | 367.5833 | 866 | 2974.1667 | 4509.1667 | 3614.1667 | 1530 | 838.5833 | 611.4167
INCM3 | 600 | 436.75 | 284.9 | 131.325 | 380.6667 | 563.0833 | 3800.8333 | 5460.8333 | 4088.3333 | 2101.6667 | 1024.4167 | 651.5
GIAOM | 600 | 374.525 | 225.2667 | 137.225 | 347.1667 | 545 | 3569.1667 | 4948.3333 | 5399.1667 | 2298.3333 | 1029.5 | 628
MIMR | 598.8333 | 405.0833 | 197.425 | 154.525 | 362.1667 | 545.9167 | 3727.5 | 5799.1667 | 5402.5 | 2796.6667 | 1134.6667 | 642
MIHR | 591.5833 | 305.3667 | 95.5167 | 90.05 | 413.3333 | 593.75 | 2366.6667 | 5148.3333 | 3986.6667 | 2090.8333 | 840.75 | 626.75
Base | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333

## Slide 47: Results cont’d
Seasonal flow change
Chart: 2055
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
BCM2 | 600 | 305.125 | 62.4917 | 46.4917 | 147.6167 | 445.8333 | 1529.1667 | 4037.5 | 3685 | 1885 | 881.75 | 618.9167
CSMK3 | 595.1667 | 292.6167 | 76.75 | 59.2167 | 297.4167 | 774.0833 | 2860.9167 | 4740 | 3774.1667 | 1785 | 835.1667 | 610.3333
INCM3 | 606.5 | 437.9 | 322.0917 | 165.0417 | 394.0833 | 535.1667 | 2941.6667 | 5505.8333 | 4354.1667 | 2270 | 1047.8333 | 698.5
GIAOM | 585 | 268.3333 | 109.1583 | 82.6583 | 324 | 468.75 | 1419.5 | 3665 | 3496.6667 | 1623.3333 | 775.5 | 609.3333
MIMR | 600 | 374.9833 | 101.7 | 66.4 | 305.9167 | 516.25 | 3776.6667 | 5684.1667 | 5435.8333 | 2661.6667 | 1085.5 | 636.9167
MIHR | 600 | 436.4167 | 156.8167 | 61.7167 | 339.75 | 617.3333 | 2786.6667 | 5195.8333 | 5346.6667 | 2826.6667 | 1123.1667 | 703.1667
Base | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333

## Slide 48: Results cont’d
Seasonal flow change
Chart: 2090
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
BCM2 | 570.9167 | 218.8083 | 74.9917 | 38.8917 | 183.1417 | 453.8333 | 1471 | 4071.6667 | 2975 | 1455.8333 | 736.3333 | 604.9167
CSMK3 | 589.0833 | 231.9333 | 75.925 | 48.1 | 228.4167 | 521.9167 | 2066.1667 | 4338.3333 | 3261.6667 | 1627.5 | 825.0833 | 607.25
INCM3 | 615.75 | 556.0833 | 427.2083 | 211.1167 | 417 | 542.1667 | 3600.8333 | 6117.5 | 5395 | 2587.5 | 1328.25 | 807.0833
GIAOM | 598.3333 | 332.0417 | 153.8917 | 131.4167 | 269.3333 | 416.75 | 2075.1667 | 4800 | 4627.5 | 2222.5 | 1014.1667 | 651.8333
MIMR | 600 | 413.025 | 91.5 | 50.725 | 278.5833 | 528.25 | 4352.5 | 7018.3333 | 6660.8333 | 3361.6667 | 1289.1667 | 687.3333
MIHR | 600 | 361.8667 | 74.0667 | 59.3833 | 285.25 | 442.4167 | 1934.1667 | 5407.5 | 5240.8333 | 2585.8333 | 984.4167 | 640.75
Base | 383.3333 | 371 | 298.5 | 209.6667 | 278.3333 | 709.3333 | 2662.8333 | 5550.1667 | 4224 | 1952.8333 | 957.6667 | 514.8333

## Slide 49: Results cont’d
Model evaluation
Climate change anaysis
Land use and cover (LUC) change analysis
Land use change analysis coupled with climate change

## Slide 50: Results cont’d
Annual yield change
Land-use Scenario | Annual WYLD (mm) | Change in Savana forest % | ∆WYLD %
Baseline (1961-90) | 223.4 | 0 | 0
LUS-1 (2080) | 189.6 | 10 | -15
LUS-2 (2080) | 249.9 | -8 | 12

## Slide 51: Results cont’d
Seasonal flow change
Chart: Discharge (m³/s)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Baseline | 595.6667 | 323.6 | 110.1667 | 77.3833 | 391.5 | 575.5 | 3163.3333 | 5060 | 4298.3333 | 2065 | 929 | 612.8333
LUS-1 | 579.1667 | 237.6833 | 79.1167 | 67.4667 | 302.1667 | 531.3333 | 2425 | 4496.6667 | 3810 | 1810 | 835.6667 | 603.5
LUS-2 | 600 | 378.5667 | 136.2833 | 85.5333 | 426.6667 | 679.5 | 3711.6667 | 5453.3333 | 4698.3333 | 2281.6667 | 1015.5 | 623

## Slide 52: Results cont’d
Model evaluation
Climate change anaysis
Land use and cover (LUC) change analysis
Land use change analysis coupled with climate change

## Slide 53: Results cont’d
Annual yield change
GCMs | LUS | Climate Change |  | Land use Change | Annual WYLD (mm) | ∆WYLD%
 |  | ∆P% | ∆T% | ∆SAVA% |  | 
BCM2 | 1 | 0.1 | 1.7 | 10 | 158.9 | -37.0
 | 2 | 0.1 | 1.7 | -8 | 216.5 | -14.2
MIMR | 1 | 3.2 | 1.2 | 10 | 276.7 | 9.7
 | 2 | 3.2 | 1.2 | -8 | 337.1 | 33.6
MIHR | 1 | 10.5 | 2.5 | 10 | 207.8 | -17.6
 | 2 | 10.5 | 2.5 | -8 | 274.2 | 8.7

## Slide 54: Results cont’d
Seasonal flow change
Chart: Discharge (m³/s)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Baseline | 595.6667 | 323.6 | 110.1667 | 77.3833 | 391.5 | 575.5 | 3163.3333 | 5060 | 4298.3333 | 2065 | 929 | 612.8333
BCM2-LUS1 | 536.8333 | 168.7167 | 59.4833 | 41.45 | 184.8333 | 442.6667 | 1160.3333 | 3743.3333 | 2475 | 1349 | 702 | 600
BCM2-LUS2 | 599.3333 | 301.0833 | 86.25 | 45.95 | 274.3333 | 521.3333 | 2311.6667 | 4741.6667 | 3341.6667 | 1878.3333 | 894.8333 | 619.1667
MIMR-LUS1 | 587.6667 | 285.7667 | 57.9667 | 49.4167 | 254.8333 | 504.8333 | 3416.6667 | 5960 | 4960 | 2293.3333 | 966.5 | 624.3333
MIMR-LUS2 | 600 | 416.8333 | 101.15 | 55.5333 | 380 | 552.8333 | 4751.6667 | 6908.3333 | 5911.6667 | 2818.3333 | 1156.6667 | 664.1667
MIHR-LUS1 | 579.8333 | 260.8333 | 72.9833 | 54.0333 | 289.6667 | 474 | 1407 | 4620 | 3921.6667 | 1891.6667 | 805.1667 | 614
MIHR-LUS2 | 600 | 405.8333 | 133.5167 | 63.15 | 410 | 542.1667 | 2620 | 5711.6667 | 5006.6667 | 2566.6667 | 1025.6667 | 694.5

## Slide 55
Introduction
Problem statement and objectives
Materials and methods
Results and discussion
Conclusion and recommendations
1
2
3
4
5

## Slide 56: Conclusion
  The SWAT model has been successfully evaluated
    Satisfactory performance - minimum NSE=0.7
    But high flow predictions were not as good as low flow predictions
Land use and climate change scenarios - helped to better understand the impact of climate change and land use change on Blue Nile river
It has been proven that land use and cover (LUC) changes as well as climate change has resulted in significant changes (either by increasing or decreasing) in the hydrology of the basin

## Slide 57: Recommendations
use of long time series and good quality data in the hydrologic models
investigate the reasons of underestimation of peak flows for Blue Nile
It will be of great importance to incorporate other factors in the assessment like, sediment transport and water quality analysis.
Incorporating the newly constructed dam by Ethiopia (GERD) in the already built hydrologic model and analyzing the impact (on development)

## Slide 58
Thanks for listening!