## Slide 1
Impact of Climate Change on the Ecohydrology of the Nile River Basin
Shimelis G Setegn, Ph.D.
Senior Scientist, SFWMD
Assistant Professor, FIU

## Slide 2: Presentation Outline
Introduction
Upstream Catchment degradation
Climate Change in the Nile
Modeling tools
Impact of climate change
Adaptation strategies

## Slide 3
Deforestation, Soil erosion - land degradation
Climate Change
Major threats in the Nile Basin

## Slide 4: Impact of soil erosion
Land and water degradation are the major issues in the Upper Nile due to deforestation and soil erosion.
Poor land use practices and improper management systems have played a significant role in causing high soil erosion rates, sediment transport and loss of agricultural nutrients.
Studies indicated that Ethiopia loses about 1.3 billion metric tons of fertile soil every year and the degradation of land through soil erosion is increasing at a high rate, Hurni (1989)

## Slide 5: River flow with high sediment concentration

## Slide 7
Lake Alemaya
Lake Adele
Degradation in water bodies due to hydrological and environmental changes

## Slide 8: Emboch
the top 250 lake regions of Global Importance for Biodiversity
the aquatic biodiversity at extreme risk due to invasion of Emboch – Aquatic weed (water hyacinth)

## Slide 9: Modeling Tools
Soil water Assessment Tool – SWAT
Generalized Environmental Modeling System for Surface waters (GEMSS)
GIS based - Multi criteria Evaluation

## Slide 10: SWAT (Soil water Assessment Tool)
SWAT is a river basin scale developed to predict the impact of land management practices on water, sediment and agricultural chemical yields
The SWAT system (ArcSWAT), embedded within geographic information system (GIS),
  can integrate various spatial environmental data

## Slide 11
GEMSS - Generalized Environmental Modeling System for Surface waters
GEMSS is an integrated system of 3-D hydrodynamic and transport modules embedded in GIS
The hydrodynamic and transport relationships used in GEMSS are developed from
  the horizontal momentum balance,
  continuity,
  constituent transport and
  the equation of state.

## Slide 12
MCE-GIS tool for Decision support system
Multi-Criteria Evaluation (MCE) is a method for decision support
  number of different criteria are combined to meet one or several objectives.
The decision was made after combination of four criteria (factor maps): Slope, Landcover, Soil types and River

## Slide 13: Model Input Data
GIS input files needed:
    the digital elevation model (DEM),
    land cover,
    soil layers
DEM
    delineate boundaries,
    stream network
    calculate average slopes
Land use, Soil and Slope layers
    to create and define Hydrological Response Units (HRU’s).

## Slide 14
Soil physical properties
  Number of layers in the soil
  Soil hydrologic group (A, B, C, D)
  Maximum rooting depth of soil profile
  Texture of soil layer
  Depth from soil surface to bottom of layer
  Moist bulk density
  Available water capacity of the soil layer
  Saturated hydraulic conductivity
  Organic carbon content
  Clay content, Silt content,
  Sand content
Model Input cont.

## Slide 15
Meteorological Data
  precipitation
  air temperature
  solar radiation
  wind speed and
  relative humidity
Model Input cont.

## Slide 16: Model Input Data
Hydrological Data
  River Discharge and
  Suspended sediment load
Land Management
data for management practices such as planting, harvest, tillage operations, and pesticide and fertilizer application.

## Slide 17: Time series of measured and simulated flow, Gilgel Abay

## Slide 18
The annual average simulated sediment yield was 28.7
Calibration period: NSE=0.81, PBIAS=28 %, RSR=0.23 & R²=0.85
Validation period: NSE=0.79, PBIAS=30 %, RSR=0.29 & R²=0.80
Comparison between measured and simulated monthly sediment yield
Sediment Yield Modeling

## Slide 19
Erosion vulnerable areas in Lake Tana Basin, Ethiopia
SWAT=18.4 %
MCE=25%

## Slide 20
Climate Change
30 August 2010, Gran Melia, Puerto Rico, photo by Shimelis S

## Slide 21
Climate change is a significant change in the statistical distribution of weather patterns over periods. eg. weather conditions or the distribution of extreme events.
Climate Change

## Slide 22: Climate Change
By 2040 the share of people in the Nile region facing water scarcity could reach 35%. That’s more than 80 million people, Coffel and Mankin 2020
250 million people rely on the Nile for water that may not exist by 2080, Zoë Schlanger 2019

## Slide 23
Increased evaporation & changes in rainfall, has the potential to affect runoff, floods and droughts
Effect of climate change
A major effect of climate change is alterations in hydrologic cycles and changes in water availability.

## Slide 24
Assessing the impact of climate change involves
  Projections of climatic variables (e.g. precipitation, temperature) at a global scale.
  Downscaling of global-scale climatic variables to local-scale hydrologic variables
Assessment of impact of climate change

## Slide 25
Projected changes

## Slide 26
Decreasing rainfall trend
Projected seasonal changes in rainfall
B1 A1B A2

## Slide 27
Increasing Temperature (0.6 – 2.8 C)
Projected seasonal changes temperature
B1 A1B A2

## Slide 28
Variation among
GCM outputs for different SRES - Precipitation/
Rainfall

## Slide 29
Impact of Climate Change on Water Resources

## Slide 30: Water Resources and Climate Change Blue Nile – Lake Tana
ETHIOPIA - Lake Tana Basin
Lake Tana basin comprises an area of 15096 km2
The lake is a natural type
  Average area = 3300 km2
  Maximum depth = 14 m.
  Inflow Rivers are GilgelAbay, Ribb, Gumera, Megech

## Slide 31
Impact of Climate Change on Surface and Ground Water 2046-2065

## Slide 33: Hydrodynamics of Lake Tana - using Combined SWAT and GEMSS model

## Slide 34
Lake Tana: flow discharge hydrographs of the inflow rivers and the lake outlet for year 2006, the positions of meteorological station and the water withdrawal tunnel (under construction).

## Slide 35
The velocity vectors in cm/s at the water surface, Feb. 10, 2006.
Flow Structures

## Slide 36
Temperature contours and the velocity vectors, section S5, January 2, 2006), legend color in °C.

## Slide 37
Contours of dye concentration (mg/l) at the water surface December 31, 2006.
Flushing Time

## Slide 38: Adaptation strategies - Measures
Appropriate catchment treatment strategies should be implemented
  Watershed management methods like afforestation and water conservation are recommended to reduce the impact on the Blue Nile basin.
create an equitable water allocation scheme upstream and downstream countries.
  “historical rights” –Egypt’s long-held claims need to be revised so that the needs of upstream countries like South Sudan and Ethiopia, which require water to build their economies, should be highly considered
  Water may be often pointed to as a source of conflict, but it can also be a means to cooperation, getting nations to the negotiating table.
  Any intervention and planning strategies should highly consider the short and long-term climate variability and change

## Slide 39
Thank You!